## Slide 2
LAN Technologies
Spanning Tree Protocol (STP) Tutorial
  STP Features:
  Port-fast
  BPDU Guard
  Root Guard
Rapid Spanning Tree Protocol (RSTP) Tutorial
Virtual Local Area Network (VLAN) Tutorial
  Trunk port
  Access port
  Default VLAN
  Native VLAN
Inter VLAN Routing
VLAN Trunking Protocol (VTP) Tutorial
EtherChannel
  LACP (Link Aggregation Control Protocol)
LLDP (Link Layer Discovery Protocol)

## Slide 3: Module Objectives
Module Title: STP Concepts
Module Objective: Explain how STP enables redundancy in a Layer 2 network.
Topic Title | Topic Objective
Purpose of STP | Explain common problems in a redundant, L2 switched network.
STP Operations | Explain how STP operates in a simple switched network.
Evolution of STP | Explain how Rapid PVST+ operates.
Notes: 3

## Slide 4: Purpose of STP Redundancy in Layer 2 Switched Networks
This topic covers the causes of loops in a Layer 2 network and briefly explains how spanning tree protocol works. Redundancy is an important part of the hierarchical design for eliminating single points of failure and preventing disruption of network services to users. Redundant networks require the addition of physical paths, but logical redundancy must also be part of the design. Having alternate physical paths for data to traverse the network makes it possible for users to access network resources, despite path disruption. However, redundant paths in a switched Ethernet network may cause both physical and logical Layer 2 loops.
Ethernet LANs require a loop-free topology with a single path between any two devices. A loop in an Ethernet LAN can cause continued propagation of Ethernet frames until a link is disrupted and breaks the loop.
Notes: 5 – STP Concepts
5.1 – Purpose of STP
5.1.1 – Redundancy in Layer 2 Switched Networks

## Slide 5: Purpose of STP Spanning Tree Protocol
Spanning Tree Protocol (STP) is a loop-prevention network protocol that allows for redundancy while creating a loop-free Layer 2 topology.
STP logically blocks physical loops in a Layer 2 network, preventing frames from circling the network forever.
Notes: 5 – STP Concepts
5.1 – Purpose of STP
5.1.2 – Spanning Tree Protocol

## Slide 6: Purpose of STP STP Recalculation
STP compensates for a failure in the network by recalculating and opening up previously blocked ports.
Notes: 5 – STP Concepts
5.1 – Purpose of STP
5.1.3 – STP Recalculation

## Slide 7: Purpose of STP Issues with Redundant Switch Links
Path redundancy provides multiple network services by eliminating the possibility of a single point of failure. When multiple paths exist between two devices on an Ethernet network, and there is no spanning tree implementation on the switches, a Layer 2 loop occurs. A Layer 2 loop can result in MAC address table instability, link saturation, and high CPU utilization on switches and end-devices, resulting in the network becoming unusable.
Layer 2 Ethernet does not include a mechanism to recognize and eliminate endlessly looping frames. Both IPv4 and IPv6 include a mechanism that limits the number of times a Layer 3 networking device can retransmit a packet. A router will decrement the TTL (Time to Live) in every IPv4 packet, and the Hop Limit field in every IPv6 packet. When these fields are decremented to 0, a router will drop the packet. Ethernet and Ethernet switches have no comparable mechanism for limiting the number of times a switch retransmits a Layer 2 frame. STP was developed specifically as a loop prevention mechanism for Layer 2 Ethernet.
Notes: 5 – STP Concepts
5.1 – Purpose of STP
5.1.4 – Issues with Redundant Switch Links

## Slide 8: Purpose of STP Layer 2 Loops
Without STP enabled, Layer 2 loops can form, causing broadcast, multicast and unknown unicast frames to loop endlessly. This can bring down a network quickly.
When a loop occurs, the MAC address table on a switch will constantly change with the updates from the broadcast frames, which results in MAC database instability. This can cause high CPU utilization, which makes the switch unable to forward frames.
An unknown unicast frame is when the switch does not have the destination MAC address in its MAC address table and must forward the frame out all ports, except the ingress port.
Notes: 5 – STP Concepts
5.1 – Purpose of STP
5.1.5 – Layer 2 Loops

## Slide 9: Purpose of STP Broadcast Storm
A broadcast storm is an abnormally high number of broadcasts overwhelming the network during a specific amount of time. Broadcast storms can disable a network within seconds by overwhelming switches and end devices. Broadcast storms can be caused by a hardware problem such as a faulty NIC or from a Layer 2 loop in the network.
Layer 2 broadcasts in a network, such as ARP Requests are very common. Layer 2 multicasts are typically forwarded the same way as a broadcast by the switch. IPv6 packets are never forwarded as a Layer 2 broadcast, ICMPv6 Neighbor Discovery uses Layer 2 multicasts.
A host caught in a Layer 2 loop is not accessible to other hosts on the network. Additionally, due to the constant changes in its MAC address table, the switch does not know out of which port to forward unicast frames.
To prevent these issues from occurring in a redundant network, some type of spanning tree must be enabled on the switches. Spanning tree is enabled, by default, on Cisco switches to prevent Layer 2 loops from occurring.
Notes: 5 – STP Concepts
5.1 – Purpose of STP
5.1.6 – Broadcast Storm

## Slide 10: Purpose of STP The Spanning Tree Algorithm
STP is based on an algorithm invented by Radia Perlman while working for Digital Equipment Corporation, and published in the 1985 paper "An Algorithm for Distributed Computation of a Spanning Tree in an Extended LAN.” Her spanning tree algorithm (STA) creates a loop-free topology by selecting a single root bridge where all other switches determine a single least-cost path.
STP prevents loops from occurring by configuring a loop-free path through the network using strategically placed "blocking-state" ports. The switches running STP are able to compensate for failures by dynamically unblocking the previously blocked ports and permitting traffic to traverse the alternate paths.
Notes: 5 – STP Concepts
5.1 – Purpose of STP
5.1.7 – The Spanning Tree Algorithm

## Slide 11: Purpose of STP The Spanning Tree Algorithm (Cont.)
How does the STP create a loop-free topology?
Selecting a Root Bridge: This bridge (switch) is the reference point for the entire network to build a spanning tree around.
Block Redundant Paths: STP ensures that there is only one logical path between all destinations on the network by intentionally blocking redundant paths that could cause a loop. When a port is blocked, user data is prevented from entering or leaving that port.
Create a Loop-Free Topology: A blocked port has the effect of making that link a non-forwarding link between the two switches. This creates a topology where each switch has only a single path to the root bridge, similar to branches on a tree that connect to the root of the tree.
Recalculate in case of Link Failure: The physical paths still exist to provide redundancy, but these paths are disabled to prevent the loops from occurring. If the path is ever needed to compensate for a network cable or switch failure, STP recalculates the paths and unblocks the necessary ports to allow the redundant path to become active. STP recalculations can also occur any time a new switch or new inter-switch link is added to the network.
Notes: 5 – STP Concepts
5.1 – Purpose of STP
5.1.7 – The Spanning Tree Algorithm (Cont.)

## Slide 12: STP Operations Steps to a Loop-Free Topology
Using the STA, STP builds a loop-free topology in a four-step process:
  Elect the root bridge.
  Elect the root ports.
  Elect designated ports.
  Elect alternate (blocked) ports.
During STA and STP functions, switches use Bridge Protocol Data Units (BPDUs) to share information about themselves and their connections. BPDUs are used to elect the root bridge, root ports, designated ports, and alternate ports.
Each BPDU contains a bridge ID (BID) that identifies which switch sent the BPDU. The BID is involved in making many of the STA decisions including root bridge and port roles.
The BID contains a priority value, the MAC address of the switch, and an extended system ID. The lowest BID value is determined by the combination of these three fields.
Notes: 5 – STP Concepts
5.2 – STP Operations
5.2.1 – Steps to a Loop-Free Topology

## Slide 13: STP Operations Steps to a Loop-Free Topology (Cont.)
Bridge Priority: The default priority value for all Cisco switches is the decimal value 32768. The range is 0 to 61440 in increments of 4096. A lower bridge priority is preferable. A bridge priority of 0 takes precedence over all other bridge priorities.
Extended System ID: The extended system ID value is a decimal value added to the bridge priority value in the BID to identify the VLAN for this BPDU.
MAC address: When two switches are configured with the same priority and have the same extended system ID, the switch having the MAC address with the lowest value, expressed in hexadecimal, will have the lower BID.
Notes: 5 – STP Concepts
5.2 – STP Operations
5.2.1 – Steps to a Loop-Free Topology (Cont.)

## Slide 14: STP Operations 1. Elect the Root Bridge
The STA designates a single switch as the root bridge and uses it as the reference point for all path calculations. Switches exchange BPDUs to build the loop-free topology beginning with selecting the root bridge.
All switches in the broadcast domain participate in the election process. After a switch boots, it begins to send out BPDU frames every two seconds. These BPDU frames contain the BID of the sending switch and the BID of the root bridge, known as the Root ID.
The switch with the lowest BID will become the root bridge. At first, all switches declare themselves as the root bridge with their own BID set as the Root ID. Eventually, the switches learn through the exchange of BPDUs which switch has the lowest BID and will agree on one root bridge.
Notes: 5 – STP Concepts
5.2 – STP Operations
5.2.2 – 1. Elect the Root Bridge

## Slide 15: STP Operations Impact of Default BIDs
Because the default BID is 32768, it is possible for two or more switches to have the same priority. In this scenario, where the priorities are the same, the switch with the lowest MAC address will become the root bridge. The administrator should configure the desired root bridge switch with a lower priority.
In the figure, all switches are configured with the same priority of 32769. Here the MAC address becomes the deciding factor as to which switch becomes the root bridge. The switch with the lowest hexadecimal MAC address value is the preferred root bridge. In this example, S2 has the lowest value for its MAC address and is elected as the root bridge for that spanning tree instance.
Note: The priority of all the switches is 32769. The value is based on the 32768 default bridge priority and the extended system ID (VLAN 1 assignment) associated with each switch (32768+1).
32769
Notes: 5 – STP Concepts
5.2 – STP Operations
5.2.3 – Impact of Default BIDs

## Slide 16: STP Operations Determine the Root Path Cost
When the root bridge has been elected for a given spanning tree instance, the STA starts determining the best paths to the root bridge from all destinations in the broadcast domain. The path information, known as the internal root path cost, is determined by the sum of all the individual port costs along the path from the switch to the root bridge.
When a switch receives the BPDU, it adds the ingress port cost of the segment to determine its internal root path cost.
The default port costs are defined by the speed at which the port operates. The table shows the default port costs suggested by IEEE. Cisco switches by default use the values as defined by the IEEE 802.1D standard, also known as the short path cost, for both STP and RSTP.
Although switch ports have a default port cost associated with them, the port cost is configurable. The ability to configure individual port costs gives the administrator the flexibility to manually control the spanning tree paths to the root bridge.
Link Speed | STP Cost: IEEE 802.1D-1998 | RSTP Cost: IEEE 802.1w-2004
10 Gbps | 2 | 2,000
1 Gbps | 4 | 20,000
100 Mbps | 19 | 200,000
10 Mbps | 100 | 2,000,000
Notes: 5 – STP Concepts
5.2 – STP Operations
5.2.4 – Determine the Root Path Cost

## Slide 17: STP Operations 2. Elect the Root Ports
After the root bridge has been determined, the STA algorithm is used to select the root port. Every non-root switch will select one root port. The root port is the port closest to the root bridge in terms of overall cost to the root bridge. This overall cost is known as the internal root path cost.
The internal root path cost is equal to the sum of all the port costs along the path to the root bridge, as shown in the figure. Paths with the lowest cost become preferred, and all other redundant paths are blocked. In the example, the internal root path cost from S2 to the root bridge S1 over path 1 is 19 while the internal root path cost over path 2 is 38. Because path 1 has a lower overall path cost to the root bridge, it is the preferred path and F0/1 becomes the root port on S2.
Notes: 5 – STP Concepts
5.2 – STP Operations
5.2.5 – 2. Elect the Root Ports

## Slide 18: STP Operations 3. Elect Designated Ports
Every segment between two switches will have one designated port. The designated port is a port on the segment that has the internal root path cost to the root bridge. In other words, the designated port has the best path to receive traffic leading to the root bridge.
What is not a root port or a designated port becomes an alternate or blocked port.
All ports on the root bridge are designated ports.
If one end of a segment is a root port, the other end is a designated port.
All ports attached to end devices are designated ports.
On segments between two switches where neither of the switches is the root bridge, the port on the switch with the least-cost path to the root bridge is a designated port.
Notes: 5 – STP Concepts
5.2 – STP Operations
5.2.6 – Elect Designated Ports

## Slide 19: STP Operations 4. Elect Alternate (Blocked) Ports
If a port is not a root port or a designated port, then it becomes an alternate (or backup) port. Here lowest bridge ID will choose as designated port. As per the image, S2 switch having the lowest bridge ID so on S3 switch. F0/2 will be blocked. Alternate ports are in discarding or blocking state to prevent loops. In the figure, the STA has configured port F0/2 on S3 in the alternate role. Port F0/2 on S3 is in the blocking state and will not forward Ethernet frames. All other inter-switch ports are in forwarding state. This is the loop-prevention part of STP.
Notes: 5 – STP Concepts
5.2 – STP Operations
5.2.7 – Elect Alternate (Blocked) Ports

## Slide 20: STP Operations Elect a Root Port from Multiple Equal-Cost Paths
When a switch has multiple equal-cost paths to the root bridge, the switch will determine a port using the following criteria:
Lowest sender BID
Lowest sender port priority
Lowest sender port ID
Notes: 5 – STP Concepts
5.2 – STP Operations
5.2.8 – Elect a Root Port from Multiple Equal-Cost Paths

## Slide 21: STP Operations Elect a Root Port from Multiple Equal-Cost Paths (Cont.)
Lowest Sender BID: This topology has four switches with switch S1 as the root bridge. Port F0/1 on switch S3 and port F0/3 on switch S4 have been selected as root ports because they have the root path cost to the root bridge for their respective switches. S2 has two ports, F0/1 and F0/2 with equal cost paths to the root bridge. The bridge IDs of S3 and S4, will be used to break the tie. This is known as the sender’s BID. S3 has a BID of 32769.5555.5555.5555 and S4 has a BID of 32769.1111.1111.1111. Because S4 has a lower BID, the F0/1 port of S2, which is the port connected to S4, will be the root port.
Notes: 5 – STP Concepts
5.2 – STP Operations
5.2.8 – Elect a Root Port from Multiple Equal-Cost Paths (Cont.)

## Slide 22: STP Operations Elect a Root Port from Multiple Equal-Cost Paths (Cont.)
Lowest Sender Port Priority: This topology has two switches which are connected with two equal-cost paths between them. S1 is the root bridge, so both of its ports are designated ports.
S4 has two ports with equal-cost paths to the root bridge. Because both ports are connected to the same switch, the sender’s BID (S1) is equal. So the first step is a tie.
Next, is the sender’s (S1) port priority. The default port priority is 128, so both ports on S1 have the same port priority. This is also a tie. However, if either port on S1 was configured with a lower port priority, S4 would put its adjacent port in forwarding state. The other port on S4 would be a blocking state.
32769
100
X
Designated port
Notes: 5 – STP Concepts
5.2 – STP Operations
5.2.8 – Elect a Root Port from Multiple Equal-Cost Paths (Cont.)

## Slide 23: STP Operations Elect a Root Port from Multiple Equal-Cost Paths (Cont.)
Lowest Sender Port ID: The last tie-breaker is the lowest sender’s port ID. Switch S4 has received BPDUs from port F0/1 and port F0/2 on S1. The decision is based on the sender’s port ID, not the receiver’s port ID. Because the port ID of F0/1 on S1 is lower than port F0/2, the port F0/6 on switch S4 will be the root port. This is the port on S4 that is connected to the F0/1 port on S1.
Port F0/5 on S4 will become an alternate port and placed in the blocking state.
Notes: 5 – STP Concepts
5.2 – STP Operations
5.2.8 – Elect a Root Port from Multiple Equal-Cost Paths (Cont.)

## Slide 24: STP Operations STP Timers and Port States
STP convergence requires three timers, as follows:
Hello Timer -The hello time is the interval between BPDUs. The default is 2 seconds but can be modified to between 1 and 10 seconds.
Forward Delay Timer -The forward delay is the time that is spent in the listening and learning state. The default is 15 seconds but can be modified to between 4 and 30 seconds.
Max Age Timer -The max age is the maximum length of time that a switch waits before attempting to change the STP topology. The default is 20 seconds but can be modified to between 6 and 40 seconds.
Note: The default times can be changed on the root bridge, which dictates the value of these timers for the STP domain.
Notes: 5 – STP Concepts
5.2 – STP Operations
5.2.9 – STP Timers and Port States

## Slide 25: STP Operations STP Timers and Port States (Cont.
STP facilitates the logical loop-free path throughout the broadcast domain. The spanning tree is determined through the information learned by the exchange of the BPDU frames between the interconnected switches. If a switch port transitions directly from the blocking state to the forwarding state without information about the full topology during the transition, the port can temporarily create a data loop. For this reason, STP has five ports states, four of which are operational port states as shown in the figure. The disabled state is considered non-operational.
Notes: 5 – STP Concepts
5.2 – STP Operations
5.2.9 – STP Timers and Port States (Cont.)

## Slide 26: STP Operations Operational Details of Each Port State
The table summarizes the operational details of each port state
Port State | BPDU | MAC Address Table | Forwarding Data Frames
Blocking | Receive only | No update | No
Listening | Receive and send | No update | No
Learning | Receive and send | Updating table | No
Forwarding | Receive and send | Updating table | Yes
Disabled | None sent or received | No update | No
Notes: 5 – STP Concepts
5.2 – STP Operations
5.2.10 – Operational Details of Each Port State

## Slide 27: STP Operations Per-VLAN Spanning Tree
STP can be configured to operate in an environment with multiple VLANs. In Per-VLAN Spanning Tree (PVST) versions of STP, there is a root bridge elected for each spanning tree instance. This makes it possible to have different root bridges for different sets of VLANs. STP operates a separate instance of STP for each individual VLAN. If all ports on all switches are members of VLAN 1, then there is only one spanning tree instance.
Notes: 5 – STP Concepts
5.2 – STP Operations
5.2.11 – Per-VLAN Spanning Tree
5.2.12 – Check Your Understanding – STP Operations

## Slide 28: Evolution of STP Different Versions of STP
Many professionals generically use spanning tree and STP to refer to the various implementations of spanning tree, such as Rapid Spanning Tree Protocol (RSTP) and Multiple Spanning Tree Protocol (MSTP). In order to communicate spanning tree concepts correctly, it is important to refer to the implementation or standard of spanning tree in context.
The latest IEEE documentation on spanning tree (IEEE-802-1D-2004) says, "STP has now been superseded by the Rapid Spanning Tree Protocol (RSTP)."The IEEE uses "STP" to refer to the original implementation of spanning tree and "RSTP" to describe the version of spanning tree specified in IEEE-802.1D-2004.
Because the two protocols share much of the same terminology and methods for the loop-free path, the primary focus will be on the current standard and the Cisco proprietary implementations of STP and RSTP.
Cisco switches running IOS 15.0 or later, run PVST+ by default. This version incorporates many of the specifications of IEEE 802.1D-2004, such as alternate ports in place of the former non-designated ports. Switches must be explicitly configured for rapid spanning tree mode in order to run the rapid spanning tree protocol.
Notes: 5 – STP Concepts
5.3 – Evolution of STP
5.3.1 – Different Versions of STP

## Slide 29: Evolution of STP Different Versions of STP (Cont.)
STP Variety | Description
STP | This is the original IEEE 802.1D version (802.1D-1998 and earlier) that provides a loop-free topology in a network with redundant links. Also called Common Spanning Tree (CST), it assumes one spanning tree instance for the entire bridged network, regardless of the number of VLANs.
PVST+ | Per-VLAN Spanning Tree (PVST+) is a Cisco enhancement of STP that provides a separate 802.1D spanning tree instance for each VLAN configured in the network. PVST+ supports PortFast, UplinkFast, BackboneFast, BPDU guard, BPDU filter, root guard, and loop guard.
802.1D-2004 | This is an updated version of the STP standard, incorporating IEEE 802.1w.
RSTP | Rapid Spanning Tree Protocol (RSTP) or IEEE 802.1w is an evolution of STP that provides faster convergence than STP.
Rapid PVST+ | This is a Cisco enhancement of RSTP that uses PVST+ and provides a separate instance of 802.1w per VLAN. Each separate instance supports PortFast, BPDU guard, BPDU filter, root guard, and loop guard.
MSTP | Multiple Spanning Tree Protocol (MSTP) is an IEEE standard inspired by the earlier Cisco proprietary Multiple Instance STP (MISTP) implementation. MSTP maps multiple VLANs into the same spanning tree instance.
MST | Multiple Spanning Tree (MST) is the Cisco implementation of MSTP, which provides up to 16 instances of RSTP and combines many VLANs with the same physical and logical topology into a common RSTP instance. Each instance supports PortFast, BPDU guard, BPDU filter, root guard, and loop guard.
Notes: 5 – STP Concepts
5.3 – Evolution of STP
5.3.1 – Different Versions of STP (Cont.)

## Slide 30: Evolution of STP RSTP Concepts
RSTP (IEEE 802.1w) supersedes the original 802.1D while retaining backward compatibility. The 802.1w STP terminology remains primarily the same as the original IEEE 802.1D STP terminology. Most parameters have been left unchanged. Users that are familiar with the original STP standard can easily configure RSTP. The same spanning tree algorithm is used for both STP and RSTP to determine port roles and topology.
RSTP increases the speed of the recalculation of the spanning tree when the Layer 2 network topology changes. RSTP can achieve much faster convergence in a properly configured network, sometimes in as little as a few hundred milliseconds. If a port is configured to be an alternate port it can immediately change to a forwarding state without waiting for the network to converge.
Note: Rapid PVST+ is the Cisco implementation of RSTP on a per-VLAN basis. With Rapid PVST+ an independent instance of RSTP runs for each VLAN.
Notes: 5 – STP Concepts
5.3 – Evolution of STP
5.3.2 – RSTP Concepts

## Slide 31: Evolution of STP RSTP Port States and Port Roles
There are only three port states in RSTP that correspond to the three possible operational states in STP. The 802.1D disabled, blocking, and listening states are merged into a unique 802.1w discarding state.
Root ports and designated ports are the same for both STP and RSTP. However, there are two RSTP port roles that correspond to the blocking state of STP. In STP, a blocked port is defined as not being the designated or root port. RSTP has two port roles for this purpose.
Notes: 5 – STP Concepts
5.3 – Evolution of STP
5.3.3 – RSTP Port States and Port Roles

## Slide 32
Show commands:
Switch#sh spanning-tree detail
VLAN0001 is executing the ieee compatible Spanning Tree Protocol
Bridge Identifier has priority of 32768, sysid 1, 0001.9780.05C3
Configured hello time 2, max age 20, forward delay 15
Current root has priority 32769
Root port is 1 (FastEthernet0/1), cost of root path is 19
Topology change flag not set, detected flag not set
Number of topology changes 0 last change occurred 00:00:00 ago
from FastEthernet0/1
Times: hold 1, topology change 35, notification 2
hello 2, max age 20, forward delay 15
Timers: hello 0, topology change 0, notification 0, aging 300
Port 1 (FastEthernet0/1) of VLAN0001 is root forwarding
Port path cost 19, Port priority 128, Port Identifier 128.1
Designated root has priority 32769, address 0001.4284.E523
Designated bridge has priority 32769, address 0001.4284.E523
Timers: message age 16, forward delay 0, hold 0
Number of transitions to forwarding state: 1
Link type is point-to-point by default
Port 2 (FastEthernet0/2) of VLAN0001 is designated forwarding
Port path cost 19, Port priority 128, Port Identifier 128.2
Designated root has priority 32769, address 0001.4284.E523
Designated bridge has priority 32769, address 0001.9780.05C3
Designated port id is 128.2, designated path cost 19
Timers: message age 16, forward delay 0, hold 0
Number of transitions to forwarding state: 1
Link type is point-to-point by defaultS
Notes: 5 – STP Concepts
5.3 – Evolution of STP
5.3.3 – RSTP Port States and Port Roles

## Slide 33: Evolution of STP RSTP Port States and Port Roles (Cont.)
The alternate port has an alternate path to the root bridge. The backup port is a backup to a shared medium, such as a hub. A backup port is less common because hubs are now considered legacy devices.
Notes: 5 – STP Concepts
5.3 – Evolution of STP
5.3.3 – RSTP Port States and Port Roles (Cont.)

## Slide 34: Evolution of STP PortFast and BPDU Guard
When a device is connected to a switch port or when a switch powers up, the switch port goes through both the listening and learning states, each time waiting for the Forward Delay timer to expire. This delay is 15 seconds for each state for a total of 30 seconds. This can present a problem for DHCP clients trying to discover a DHCP server because the DHCP process may timeout. The result is that an IPv4 client will not receive a valid IPv4 address.
When a switch port is configured with PortFast, that port transitions from blocking to forwarding state immediately, avoiding the 30 second delay. You can use PortFast on access ports to allow devices connected to these ports to access the network immediately. PortFast should only be used on access ports. If you enable PortFast on a port connecting to another switch, you risk creating a spanning tree loop.
A PortFast-enabled switch port should never receive BPDUs because that would indicate that switch is connected to the port, potentially causing a spanning tree loop. Cisco switches support a feature called BPDU guard. When enabled, it immediately puts the switch port in an errdisabled (error-disabled) state upon receipt of any BPDU. This protects against potential loops by effectively shutting down the port. The administrator must manually put the interface back into service.
Notes: 5 – STP Concepts
5.3 – Evolution of STP
5.3.4 – PortFast and BPDU Guard

## Slide 35: Evolution of STP Alternatives to STP
Over the years, organizations required greater resiliency and availability in the LAN. Ethernet LANs went from a few interconnected switches connected to a single router, to a sophisticated hierarchical network design including access, distribution and core layer switches.
Depending on the implementation, Layer 2 may include not only the access layer, but also the distribution or even the core layers. These designs may include hundreds of switches, with hundreds or even thousands of VLANs. STP has adapted to the added redundancy and complexity with enhancements, as part of RSTP and MSTP.
An important aspect to network design is fast and predictable convergence when there is a failure or change in the topology. Spanning tree does not offer the same efficiencies and predictabilities provided by routing protocols at Layer 3.
Layer 3 routing allows for redundant paths and loops in the topology, without blocking ports. For this reason, some environments are transitioning to Layer 3 everywhere except where devices connect to the access layer switch. In other words, the connections between access layer switches and distribution switches would be Layer 3 instead of Layer 2.
Notes: 5 – STP Concepts
5.3 – Evolution of STP
5.3.5 – Alternatives to STP
5.3.6 – Check Your Understanding – Evolution of STP

## Slide 36: New Terms and Commands
Spanning Tree Protocol (STP)
Spanning Tree Algorithm (STA)
IEEE 802.1D
IEEE 802.1w
Broadcast Storm
Root Bridge
Root Port
Designated Port
Alternate (Blocked) Port
Learning
Listening
Bridge ID (BID)
Root ID
Bridge Protocol Data Unit (BPDU)
Bridge Priority
Extended System ID
short path cost
long path cost
root path cost
Rapid STP (RSTP)
port priority
Hello timer
Max Age timer
Forward Delay timers
Blocking
Forwarding
Discarding
PVST+
Rapid PVST+
Multiple Spanning Tree Protocol (MSTP)
Multiple Spanning Tree (MST)
PortFast
BPDU Guard