## Slide 2
Network Address Translation(NAT)

## Slide 3
AGENDA
NAT
Working of NAT
NAT inside and outside address
NAT types
Advantages of NAT
Disadvantages of NAT

## Slide 4
NAT:
Network Address Translation (NAT) is a service that enables private IP networks to use the internet and cloud. NAT translates one or more private IP addresses in an internal network to a public IP address before packets are sent to an external network. NAT generally operates on a Router or a Firewall.
Working of Network Address Translation (NAT):
Generally, the border router is configured for NAT i.e. the router which has one interface in the local (inside) network and one interface in the global (outside) network. When a packet traverse outside the local (inside) network, then NAT converts that local (private) IP address to a global (public) IP address. When a packet enters the local network, the global (public) IP address is converted to a local (private) IP address.
If NAT runs out of addresses, i.e., no address is left in the pool configured then the packets will be dropped and an Internet Control Message Protocol (ICMP) host unreachable packet to the destination is sent.
NAT inside and outside addresses:
Inside refers to the addresses which must be translated. Outside refers to the addresses which are not in control of an organization. These are the network Addresses in which the translation of the addresses will be done.

## Slide 5
Inside local address – An IP address that is assigned to a host on the Inside (local) network. The address is probably not an IP address assigned by the service provider i.e., these are private IP addresses. This is the inside host seen from the inside network.
Inside global address – IP address that represents one or more inside local IP addresses to the outside world. This is the inside host as seen from the outside network.
Outside local address – This is the actual IP address of the destination host in the local network after translation.
Outside global address – This is the outside host as seen from the outside network. It is the IP address of the outside destination host before translation.

## Slide 6
Network Address Translation (NAT) Types:
Static NAT
Dynamic NAT
Port Address Translation (PAT)
Static NAT:
In static NAT, a single Private IP address is mapped with a single Public IP address i.e one-to-one mapping between Private and Public IP addresses. This is generally used for Web hosting. These are not used in organizations as there are many devices that will need Internet access and to provide Internet access, a public IP address is needed.
Suppose, if there are 3000 devices that need access to the Internet, the organization has to buy 3000 public addresses that will be very costly.
Dynamic NAT:
In this type of NAT, an unregistered IP address is translated into a registered (Public) IP address from a pool of public IP addresses. This is one-to-many mapping. If the IP address of the pool is not free, then the packet will be dropped as only a fixed number of private IP addresses can be translated to public addresses.
Suppose, if there is a pool of 2 public IP addresses then only 2 private IP addresses can be translated at a given time. If 3rd private IP address wants to access the Internet then the packet will be dropped therefore many private IP addresses are mapped to a pool of public IP addresses. NAT is used when the number of users who want to access the Internet is fixed. This is also very costly as the organization has to buy many global IP addresses to make a pool.

## Slide 7
Port Address Translation (PAT)
This is also known as NAT overload. In this, many local (private) IP Addresses can be translated to a single Public IP address. Port numbers are used to distinguish the traffic i.e., which traffic belongs to which IP address. This is many-to-one mapping. This is most frequently used as it is cost-effective as thousands of users can be connected to the Internet by using only one real global (public) IP address.
Advantages of NAT:
NAT conserves legally registered IP addresses.
It provides privacy as the device’s IP address, sending and receiving the traffic, will be hidden.
Eliminates address renumbering when a network evolves.
Disadvantage of NAT:
Translation results in switching path delays.
Certain applications will not function while NAT is enabled.
Complicates tunneling protocols such as IPsec.
Also, the router being a network layer device, should not tamper with port numbers(transport layer) but it has to do so because of NAT.

## Slide 8
Lab Implementation:
R1#config terminal R1(config)#interface ethernet 1/0
R1(config-if)#ip address 10.10.10.1 255.255.255.0
R1(config-if)#no shut R1(config-if)#ip nat inside
R1(config-if)#exit R1(config)#interface ethernet 1/1
R1(config-if)#ip address 202.13.45.100 255.255.255.0
R1(config-if)#no shut R1(config-if)#ip nat outside R1(config-if)#end
R1(config)# ip nat inside source static 10.10.10.10 202.14.35.100
Verification:
R1#show ip nat statistics
R1#show ip nat translations